## Slide 1
Milling Machine

## Slide 2: Content:
Introduction of milling machine
Principle of milling machine
Types of milling machine
Milling machine operations

## Slide 3
Milling

## Slide 4
Milling machine
Milling: is a metal cutting operation in which the excess material from the work piece is removed by rotating multipoint cutting tool called milling cutter.
A milling machine is a machine tool that removes metal as the work is fed against a rotating multipoint cutter. The milling cutter rotates at high speed and it removes metal at a very fast rate with the help of multiple cutting edges.
One or more number of cutters can be mounted simultaneously on the milling machine. This is the reason that a milling machine finds wide application in production work.
Used for machining flat surfaces, contoured surfaces, external and internal threads.

## Slide 5
Milling
Milling is the process of machining flat, curved, or irregular surfaces by feeding the work piece against a rotating cutter containing a number of cutting edges. The usual Mill consists basically of a motor driven spindle, which mounts and revolves the milling cutter, and a reciprocating adjustable worktable, which mounts and feeds the work piece.
Milling machines are basically classified as vertical or horizontal. These machines are also classified as knee-type, ram-type, manufacturing or bed type, and planer-type. Most milling machines have self-contained electric drive motors, coolant systems, variable spindle speeds, and power-operated table feeds

## Slide 6
Milling machine
As the workpiece moves against the cutting edges of milling cutter, metal is removed in form chips
Machined surface is formed in one or more passes of the work.
The work to be machined is held in a vice, a rotary table, a three jaw chuck, an index head, in a special fixture or bolted to machine table.
In many applications, due to its higher production rate and accuracy, milling machine has even replaced shapers and slotters.

## Slide 7
Milling is a process of producing flat and complex shapes with the use of multi-tooth cutting tool, which is called a milling cutter and the cutting edges are called teeth.
The axis of rotation of the cutting tool is perpendicular to the direction of feed, either parallel or perpendicular to the machined surface. The machine tool that traditionally performs this operation is called milling machine.
Milling is an interrupted cutting operation in which the teeth of the milling cutter enter and exit the work during each revolution. This interrupted cutting action subjects the teeth to a cycle of impact force and thermal shock on every rotation. The tool material and cutter geometry must be designed to withstand these conditions. Cutting fluids are essential for most milling operations.

## Slide 8
Milling machine applications

## Slide 9: Milling methods
Two basic methods of milling
1.Up-milling or conventional milling
2.Down-milling or climb milling
1.Up-milling or conventional milling
Metal is removed by cutter rotating against the direction of travel of the workpiece.
Needs stronger holding of the job.
Chip thickness is minimum at the start of cut and maximum at the end of the cut.
Disadvantage- tendency to lift work from the fixtures and poor surface finish.

## Slide 10: 1.Conventional milling

## Slide 11: Milling methods
2.down-milling or climb milling
Metal is removed by cutter rotating in the same direction of travel of the workpiece.
teeth cut downward instead of upwards.
Chip thickness is maximum at the start of cut and minimum at the end of cut.
Less friction involved
Better surface finish.
Less power consumption.

## Slide 12: 2.Climb milling

## Slide 13: PRINCIPLE OF MILLING

## Slide 14
Fig. 10 Effect of milling cutter diameter on workpiece travel
Large diameter
cutter
Amount of travel using large diameter cutter
Direction of cut
Material being removed
workpiece
Small diameter
cutter
Amount of travel using small diameter cutter

## Slide 15: COMPARISON BETWEEN UP MILLING & DOWN MILLING
SL. NO. | UP MILLING (CONVENTIONAL MILLING) | DOWN MILLING (CLIMB MILLING)
01 | Work piece fed in the opposite direction that of the cutter. | Work piece fed in the same direction that of the cutter.
02 | Chips are progressively thicker. | Chips are progressively thinner.
03 | Strong clamping is required since the cutting force is directed upwards & tends to lift the work piece. | Strong clamping is not required since the cutting force is directed downwards & keep the work piece pressed to the table.
04 | Gives poor surface finish, since chips gets accumulated at the cutting zone. | Gives good surface finish, since the chips are thrown away during cutting.
05 | Used for hard materials. | Used for soft materials and finishing operations.

## Slide 16: Types of milling machine
The milling machine may be classified in several forms, but the choice of any particular machine is determined primarily by the size of the workpiece.
According to general design, the distinctive types of milling machines are:
Column and knee type milling machines
Planer type milling machine
Fixed-bed type milling machine
Special purpose milling machines
a.Tracer controlled milling machine
b. Thread milling machine
c. CNC milling machine

## Slide 17: Principle parts
Base
Column
Knee
Saddle
Table
Spindle

## Slide 18: Column and knee type
It is the most commonly used milling machine used for general shop work.
The table is mounted on the knee which in turn is mounted on the vertical slides of the main column.
The knee is vertically adjustable on the column so that the table can be moved up and down to accommodate work of various heights.

## Slide 19: Classifiaction of column & knee type milling machine
(a) Hand milling m/c.
(b) Horizontal milling m/c.
(c) Universal milling m/c.
(d) Vertical milling m/c.

## Slide 20: HORIZONTAL MILLING MACHINE
FIG. HORIZONTAL MILLING MACHINE
MAJOR PARTS :
BASE
COLUMN
SPINDLE
OVERARM
KNEE
SADDLE
WORKTABLE

## Slide 21: (a) Horizontal Milling machine
  The horizontal milling machine has a spindle that is parallel to the shop floor and an overarm that extends over the workpiece.
  The overarm supports the arbor, which holds the milling cutter.
  On the horizontal mill, the arbor is the component that rotates the milling cutter.

## Slide 23: Actual horizontal milling machine

## Slide 24: Arbors
Fig : Mounting a milling cutter on an arbor for use on a horizontal milling machine.

## Slide 25: (b) Vertical milling machine
Spindle is vertical or perpendicular to the work table.
It has all the movements of the table for proper setting and feeding the work.
Spindle head may be swiveled at an angle, permitting the milling cutter mounted on the spindle to work on angular surfaces.
In some machines, spindle can also be adjusted up or down relative to the work.
Adopted for machining grooves, slots and flat surfaces.

## Slide 26: VERTICAL MILLING MACHINE
MAJOR PARTS :
BASE
COLUMN
SPINDLE
SPINDLE HEAD
KNEE
SADDLE
WORKTABLE
FIG. VERTICAL MILLING MACHINE

## Slide 27
DIFFERENCES BETWEEN HORIZONTAL & VERTICAL MILLING MACHINES
SL. NO. | HORIZONTAL MILLING MACHINE | VERTICAL MILLING MACHINE
01 | Spindle is horizontal & parallel to the worktable. | Spindle is vertical & perpendicular to the worktable.
02 | Cutter cannot be moved up & down. | Cutter can be moved up & down.
03 | Cutter is mounted on the arbor. | Cutter is directly mounted on the spindle.
04 | Spindle cannot be tilted. | Spindle can be tilted for angular cutting.
05 | Operations such as plain milling, gear cutting, form milling, straddle milling, gang milling etc., can be performed. | Operations such as slot milling, T-slot milling, angular milling, flat milling etc., can be performed and also drilling, boring and reaming can be carried out.

## Slide 28: (c) Universal milling machine
Difference from plain horizontal machine is addition of table swivel housing Permits table to be swiveled 45º in either direction in a horizontal plane
Used for milling of helical grooves in twist drills, milling cutters, and gears

## Slide 29
2. Fixed-bed type milling machine
Comparatively large, heavy and rigid and differ from column and knee type milling machines.
Table is directly mounted on fixed bed.
No provision is provided for cross or vertical adjustment of the table.
The cutter mounted on the spindle head may be moved vertically on the column and the spindle may be adjusted horizontally to provide cross adjustment.
Three types
1. Simplex 2. duplex 3. triplex

## Slide 30: Fixed bed milling machine

## Slide 31: Planer milling machine
Looks like double column planer machine.
Milling heads mounted in various planes, vertical heads on the cross-rail and horizontal heads at the sides (on column)
This arrangement enables it to machine a workpiece on several sides simultaneously
Used for producing long straight surfaces on large and heavy machine parts.

## Slide 32: Special-Type Machines
Designed for individual milling operations
Used for only one particular type of job
Completely automatic Employed when hundreds or thousands of similar pieces are to be machined
Tracer mills (Profiling milling machines):
- Also called duplicators
- Designed to reproduce an irregular part geometry
- In two dimensions
- In three dimensions

## Slide 33: Special-Type Machines
CNC milling machines:
- Cutter path controlled by numerical data
- Suited to profile, pocket, surface contouring.

## Slide 34: MILLING OPERATIONS
Plain or slab milling
Face milling
End milling
Side milling
Slot milling
Angular milling
Form milling
Straddle milling
Gear cutting
Gang milling

## Slide 35: MILLING OPERATIONS
saw milling
Gear cutting
Key way milling
Profile milling
Thread milling
Helical milling

## Slide 36: PLAIN/SURFACE/ SLAB MILLING
Plain Milling:
Process to get the flat surface on the work piece in which the cutter axis and work piece axis are parallel. The primary motion is the rotation of the cutter. The feed is imparted to the work piece.
Cutter: Plain milling cutter.
Machine:Horizontal Milling m/c.

## Slide 37: PLAIN/SURFACE/ SLAB MILLING
Work piece
Plain mill cutter

## Slide 38: FACE MILLING
Face Milling:
Operation carried out for producing a flat surface, which is perpendicular to the axis of rotating cutter.
Cutter: Face milling cutter.
Machine: Vertical Milling Machine

## Slide 39: Face milling Manufacturing Technology

## Slide 40: FACE MILLING
FIG. FACE MILLING
Face Milling:
Operation carried out for producing a flat surface, which is perpendicular to the axis of rotating cutter.
Cutter: Face milling cutter.
Machine: Vertical Milling Machine

## Slide 41: END MILLING
FIG. END MILLING
End Milling:
Operation performed for producing flat surfaces, key slots, grooves or finishing the edges of the work piece.
Cutter: End milling cutter.
Machine: Vertical Milling Machine

## Slide 42: END MILLING
FIG. END MILLING
End Milling:
Operation performed for producing flat surfaces, slots, grooves or finishing the edges of the work piece.
Cutter: End milling cutter.
Machine: Vertical Milling Machine

## Slide 43: SIDE MILLING
SIDE MILLING : Operation performed for producing flat surfaces, slots, grooves or finishing the edges of the work piece.
Cutter: End milling cutter.
Machine: Horizontal Milling Machine

## Slide 44: SLOT MILLING
FIG. T-SLOT MILLING
Slot Milling:
Operation of producing slots like T-slots, plain slots etc.,
Cutter: End milling cutter, T-slot cutter, side milling cutter
Machine: Vertical Milling Machine

## Slide 46: ANGULAR MILLING
FIG. ANGULAR MILLING
Angular Milling:
Operation of producing all types of angular cuts like V-notches and grooves, serrations and angular surfaces.
Cutter: Double angle cutter.
Machine:Horizontal Milling Machine

## Slide 47: FORM MILLING
FIG. FORM MILLING
Form Milling:
Operation of producing all types of angular cuts like V-notches and grooves, serrations and angular surfaces.
Cutter: Double angle cutter.
Machine: Horizontal Milling Machine

## Slide 48
FORM MILLING

## Slide 49
STRADDLE MILLING
FIG. STRADDLE MILLING
Straddle Milling:
Operation of machining two parallel surfaces simultaneously on a work piece.
Cutter: 2 or more side & face milling cutters
Machine: Horizontal Milling Machine

## Slide 50: GANG MILLING
FIG. GANG MILLING
Gang Milling:
Process to get different profiles on the work piece simultaneously with two or more cutters at one stretch.
Cutter: Different cutters as required.
Machine: Horizontal Milling Machine

## Slide 51
Profile milling
Outside periphery of flat part is cut.
Conventional end mill is used to cut the outside or inside periphery of a flat part.

## Slide 52
Another form of end milling used to mill shallow pockets into flat parts
Pocket Milling

## Slide 53: Surface Contouring
Ball ‑ nose cutter is fed back and forth across the work along a curvilinear path at close intervals to create a three dimensional surface.

## Slide 54
TABLE 1 Parameters and formulae of the milling process
N | = | Rotational speed of the milling cutter, rpm
f | = | Feed, mm/tooth or in./tooth
D | = | Cutter diameter, mm or in.
n | = | Number of teeth on cutter
v | = | Linear speed of the workpiece or feed rate, mm/min or in./min
V | = | Surface speed of cutter, m/min or ft/min
 |  | =D N
f | = | Feed per tooth, mm/tooth or in/tooth
 |  | =v /N n
l | = | Length of cut, mm or in.
t | = | Cutting time, s or min
 |  | =( l+lc ) v , where lc =extent of the cutter’s first contact with workpiece
MRR | = | mm3/min or in.3/min
 |  | =w d v , where w is the width of cut
Torque | = | N-m or lb-ft
 |  | ( Fc ) (D/2)
Power | = | kW or hp
 | = | (Torque) ( ), where  = 2 N radians/min
Note: The units given are those that are commonly used; however, appropriate units must be used in the formulas.

## Slide 55: Slab milling

## Slide 57: Slab milling

## Slide 58: Slab milling
Assume that D = 200 mm, w = 30 mm, l = 600 mm, d = 2 mm, v = 1 mm/s, and N = 200 rpm. The cutter has 10 inserts, and the workpiece material is 304 stainless steel. Calculate the material removal rate, cutting time, and feed per tooth, and estimate the power required in this operation.

## Slide 59: Slab Milling
A slab milling operation is performed on the top surface of a steel rectangular work piece 12.0 in long by 2.5 in wide. The helical milling cutter, which has a 3.0 in diameter and ten teeth, is set up to overhang the width of the part on both sides. Cutting speed is 125 ft/min, feed is 0.006 in/tooth, and depth of cut = 0.300 in. Determine (a) the actual machining time to make one pass across the surface and (b) the maximum metal removal rate during the cut. (c) If an additional approach distance of 0.5 in is provided at the beginning of the pass (before cutting begins), and an over travel distance is provided at the end of the pass equal to the cutter radius plus 0.5 in, what is the duration of the feed motion.

## Slide 62: Groover Book

## Slide 63: Groover Book

## Slide 64: Problem statement
Estimate the time required for face milling an 8-in. long, 3-in. wide brass block using a 8-in diameter cutter with 12 HSS teeth.
Consider lc=√Dw and feed rate same as face milling

## Slide 65: Face milling

## Slide 66: Face milling
A face milling operation is used to machine 6.0 mm from the top surface of a rectangular piece of aluminum 300 mm long by 125 mm wide in a single pass. The cutter follows a path that is centered over the work piece. It has four teeth and is 150 mm in diameter. Cutting speed = 2.8 m/s, and chip load = 0.27 mm/tooth. Determine (a) the actual machining time to make the pass across the surface
and (b) the maximum metal removal rate during cutting.

## Slide 67: Face Milling
A face milling operation is performed on the top surface of a steel rectangular work piece 12.0 in long by 2.5 in wide. The milling cutter follows a path that is centered over the wor kpiece. It has five teeth and a 3.0 in diameter. Cutting speed = 250 ft/min, feed = 0.006 in/tooth, and depth of cut = 0.150 in. Determine (a) the actual cutting time to make one pass across the surface and (b) the maximum metal removal rate during the cut. (c) If an additional approach distance of 0.5 in is provided at the beginning of the pass (before cutting begins), and an over travel distance is provided at the end of the pass equal to the cutter radius plus 0.5 in, what is the duration of the feed motion.

## Slide 68
Your Text Here
THANK YOU